RFD900 Tools – Test Plan

# PPM
1. Single local modem:
  1. Connect a single RFD900x modem with SiK firmware to the PC.
  2. Select COM port and connect.
  3. Set to defaults.
  4. Load settings.
  5. The “Set PPM Fail Safe” button should be greyed out on the local side.
  6. The GPO1_1R/COUT check box shouldn’t be greyed out, but the box should be unchecked.
  7. Check the GPO1_1R/COUT checkbox.
  8. Save settings.
  9. The “Set PPM Fail Safe” button should be enabled.
  10. Load settings.
  11. The “Set PPM Fail Safe” button should still be enabled.
  12. Click “Set PPM Fail Safe” button.
  13. It should say “done”
  14. Uncheck the GPO1_1R/COUT checkbox.
  15. Save settings.
  16. The “Set PPM Fail Safe” button should be disabled.
  17. Load settings.
  18. The “Set PPM Fail Safe” button should still be disabled.
  19. Disconnect.
2. Two modems
  1. Get a 2nd RFD900x modem with SiK firmware and connect it to the PC (remove first one first)
  2. Select COM port and connect.
  3. Set to defaults.
  4. Disconnect
  5. Remove from PC and power on somewhere nearby.
  6. Repeat all of the steps for a single modem, ensure all tests OK.
  7. Repeat all of the steps for a single modem, but this time do everything on the remote side of the screen. Ensure all tests OK.
# RFD868X min and max frequency
1. Get a pair of RFD868X’s
2. Connect them one-by-one to the local machine and set back to default.
3. Power them both up.
4. Start the program and connect to one of them via serial port.
5. Load settings.
6. Both local and remote’s min and max frequency ranges available should be the same.
7. Change the max frequency of the local modem to anything else.
8. Go “Copy required to remote”
9. The max frequency of the remote should show the same as the local.
# Multipoint node ID and Node Destination
1. Program multipoint firmware into a modem.
2. Connect to the modem using hterm, and send it an ATI5? Command. Take note of the node ID and node destination ranges available.
3. Connect to the modem with RFD900 tools. Load settings.
4. Check that the allowed node id range is the same as that shown in hterm.
5. Check that the allowed node destination range is the same as that for node id, except it should also have one extra option which is the maximum of the range given in hterm for that parameter.